## Slide 1: IOT Road Monitoring
By Mubashir Hussain & Sarmad Alvi

## Slide 2: Road Monitoring
Need vast amounts of data to plan road works and allocate budget (12% of city budget)
Currently city uses a variety of methods to monitor traffic and road conditions
  Cameras
  Radars
  GPR
  Every few years
Data used to set timings on traffic lights, plan construction, set speed limits etc.

## Slide 3: OuR Solutions
Use various modules to record relevant data
  Vehicle speed & traction control via CAN Bus
  Pot Holes via accelerometer
  Vehicle position via GPS module
Send data using 4G to a server and record data in SQL database
Display road condition on a website for public use
Database used by municipality to do data analysis
Fit easily within a car

## Slide 4: Communication module
NB-IOT SIM7020G – 50$
SIM7600G-H – 130$

## Slide 5: Pot-hole detection
Device Alternatives: None, we aim to use accelerometer on an IMU (Inertial measurement unit)
Algorithm Alternatives
Thresholding algorithm
Neural network algorithm
MPU-6050

## Slide 6: Gps
UART GPS module
  1.8 m accuracy
  0.1 m/s accuracy
  22 tracking, 66 searching satellites
Require accurate location, stationary and moving, small size, power requirement
Alternative is assisted GPS (using cell towers) but it costs data to use

## Slide 7: Can buS
CAN Bus module made for Raspberry Pi Pico
  Built in CAN controller and transceiver
  Supports multiple versions of CAN
  Communicates over SPI
Alternative is a OBDII UART board
  Supports multiple standards used in cars (CAN BUS, K-Line, etc.)

## Slide 8: Division of labor
Mubashir Hussain
Communication Module
Pot hole detection
PCB
Sarmad Alvi
GPS
Can Bus
Back end (Database)

## Slide 9: Gantt chart

## Slide 10: Test plan
Communication Module: Connect to internet and ping public websites (ex. Google.ca) and send HTTP requests
Pot-hole detection Module: Manual hand testing to make certain peaks are responded to, calibrate sensor using actual road
GPS Module : Connect to satellites and get valid connection
Can-bus Module: Use simulated CAN data to test CAN module then test on a real car